## Slide 1: Mining Data Streams
Jiawei Han
Computer Science
University of Illinois at Urbana-Champaign
April 4, 2016

## Slide 3: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 4: Data Streams and Their Characteristics
Data Streams
  Features: Continuous, ordered, changing, fast, huge volume
  Contrast with traditional DBMS (finite, persistent data sets)
Characteristics
  Huge volumes of continuous data, possibly infinite
  Fast changing and requires fast, real-time response
  Data stream captures nicely our data processing needs of today
  Random access is expensive: single scan algorithm (can only have one look)
  Store only the summary of the data seen thus far
  Most stream data are at low-level and multi-dimensional in nature, needs multi-level and multi-dimensional processing

## Slide 5: Streaming Data Applications
Telecommunication calling records
Business: credit card transaction flows
Network monitoring and traffic engineering
Financial market: stock exchange
Engineering & industrial processes: power supply & manufacturing
Sensor, monitoring & surveillance: video streams, RFIDs
Security monitoring
Web logs and Web page click streams
Massive data sets (even saved but random access is too expensive)

## Slide 6: DBMS vs. DSMS (Data Stream Management Systems)
Persistent relations
One-time queries
Random access
“Unbounded” disk store
Only current state matters
No real-time services
Relatively low update rate
Data at any granularity
Assume precise data
Access plan determined by query processor, physical DB design
Transient streams
Continuous queries
Sequential access
Bounded main memory
Historical data is important
Real-time requirements
Possibly multi-GB arrival rate
Data at fine granularity
Data stale/imprecise
Unpredictable/variable data arrival and characteristics
Ack. From Motwani’s PODS’04 tutorial slides

## Slide 7: Stream Data Processing: An Architecture
Scratch Space
(Main memory and/or Disk)
Continuous Query
Multiple streams
User/Application
Stream Processing
System
Results
Q: How can we perform cluster analysis effectively in data streams?
Data Streams
  Continuous, ordered, changing, fast, huge volume
  Single-scan algorithm

## Slide 8: Challenges of Stream Query Processing
Multiple, continuous, rapid, time-varying, ordered streams
Main memory computations
Queries are often continuous
  Evaluated continuously as stream data arrives
  Answer updated over time
Queries are often complex
  Beyond element-at-a-time processing
  Beyond stream-at-a-time processing
  Beyond relational queries (scientific, data mining, OLAP)
Multi-level/multi-dimensional query processing
  Most stream data are at low-level or multi-dimensional in nature

## Slide 9: Stream Data Mining Tasks
Stream mining vs. stream querying
  Stream mining shares many difficulties with stream querying
    E.g., single-scan, fast response, dynamic, …
    But often requires less “precision”, e.g., no join, grouping, sorting
  Patterns are hidden and more general than querying
Stream data mining tasks
  Multi-dimensional on-line analysis of streams
  Pattern mining in data streams
  Classification of stream data
  Clustering data streams
  Mining outliers and anomalies in stream data

## Slide 10: Challenges of Mining Dynamics in Data Streams
Most stream data are at pretty low-level or multi-dimensional in nature: needs ML/MD processing
Analysis requirements
  Multi-dimensional trends and unusual patterns
  Capturing important changes at multi-dimensions/levels
  Fast, real-time detection and response
  Comparing with data cube: Similarity and differences
Stream (data) cube or stream OLAP: Is this feasible?
  Can we implement it efficiently?

## Slide 12: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 13: Multi-Dimensional Stream Analysis: Examples
Analysis of Web click streams
  Raw data at low levels: seconds, web page addresses, user IP addresses, …
  Analysts want: changes, trends, unusual patterns, at reasonable levels of details
  E.g., Average clicking traffic in North America on sports in the last 15 minutes is 40% higher than that in the last 24 hours.”
Analysis of power consumption streams
  Raw data: power consumption flow for every household, every minute
  Patterns one may find: average hourly power consumption surges up 30% for manufacturing companies in Chicago in the last 2 hours today than that of the same day a week ago

## Slide 14: A Stream Cube Architecture
A tilted time frame
  Different time granularities
    second, minute, quarter, hour, day, week, …
Critical layers
  Minimum interest layer (m-layer)
  Observation layer (o-layer)
  User: watches at o-layer and occasionally needs to drill-down down to m-layer
Partial materialization of stream cubes
  Full materialization: too space and time consuming
  No materialization: slow response at query time
  Partial materialization: what do we mean “partial”?

## Slide 15: Cube: A Lattice of Cuboids
time,item
time,item,location
time, item, location, supplier
all
time
item
location
supplier
time,location
time,supplier
item,location
item,supplier
location,supplier
time,item,supplier
time,location,supplier
item,location,supplier
0-D(apex) cuboid
1-D cuboids
2-D cuboids
3-D cuboids
4-D(base) cuboid

## Slide 16: Time Dimension: A Tilted Time Model
Tilted time frames: A trade-off between space and granularity of time
  Decide at what moments the snapshots of the statistical information are stored
Design: Natural, logarithmic and pyramidal tilted time frames
  Natural tilted time frame:
    Ex: Minimal: 15min, then 4 * 15mins  1 hour, 24 hours  day, …
  Logarithmic tilted time frame:
    Ex. Minimal: 1 minute, then 1, 2, 4, 8, 16, 32, …

## Slide 17: Two Critical Generalized Layers in the Stream Cube
Raw data stream sits at the “primitive” stream data layer
Stream data is generalized to m-layer (minimal interest layer) and “stored” to facilitate flexible drilling
Stream data should be constantly summarized and presented at the o-layer (observation layer) for constant observation
(*, theme, quarter)
(user-group, URL-group, minute)
m-layer (minimal interest)
(individual-user, URL, second)
(primitive) stream data layer
o-layer (observation)

## Slide 18: OLAP Operation and Cube Materialization
OLAP( Online Analytical Processing) operations:
  Roll up (drill-up): summarize data
    by climbing up hierarchy or by dimension reduction
  Drill down (roll down): reverse of roll-up
    from higher level summary to lower level summary or detailed data, or introducing new dimensions
  Slice and dice: project and select
  Pivot (rotate): reorient the cube, visualization, 3D to series of 2D planes
Cube partial materialization
  Store some pre-computed cuboids for fast online processing

## Slide 19: On-Line Partial Materialization
Materialization takes precious space and time
  Only incremental materialization (with tilted time frame)
Only materialize “cuboids” of the critical layers?
  Online computation may take too much time
Preferred solution:
  Popular-path approach: Materializing those along the popular drilling paths
  H-tree structure: Such cuboids can be computed and stored efficiently using the H-tree structure
Materialization on Popular Path

## Slide 20: OLAP Processing Using Stream Cubes
Online aggregation vs. query-based computation
  Online computing while streaming: aggregating stream cubes
  Query-based computation: Using computed cuboids
Minimal int. layer
root
Chicago
Urbana
Springfield
.com
.edu
.com
.gov
Elec
Chem
Elec
Bio
Observation layer
6:00AM-7:00AM 156
7:00AM-8:00AM 201
8:00AM-9:00AM 235
……
  An H-tree cubing Structure (Ref.: Han, et al., SIGMOD’01)
  Space preserving
    Intermediate aggregates can be computed incrementally and saved in tree nodes
  Facilitate computing other cells and multi-dimensional analysis
  H-tree with computed cells can be viewed as stream cube

## Slide 22: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 23: Mining Approximate Frequent Patterns
Mining precise frequent patterns in stream data: Unrealistic
  Cannot even store them in a compressed form (e.g., FPtree)
Approximate answers are often sufficient for pattern analysis
  Ex.: A router
    is interested in all flows whose frequency is at least 1% (σ) of the entire traffic stream seen so far
    and feels that 1/10 of σ (ε = 0.1%) error is comfortable
How to mine frequent patterns with good approximation?
  Lossy Counting Algorithm (Manku & Motwani, VLDB’02)
    Major ideas: Not to keep the items with very low support count
    Advantage: Guaranteed error bound
    Disadvantage: Keeping a large set of traces

## Slide 24: Lossy Counting for Frequent Single Items
Bucket 1
Bucket 2
Bucket 3
Divide stream into ‘buckets’ (bucket size is 1/ ε = 1000)
At bucket boundary, decrease all counters by 1
Empty (summary)
+
+
Next Bucket of the Stream
First Bucket of the Stream

## Slide 25: Approximation Guarantee
Given: (1) support threshold: σ, (2) error threshold: ε, and (3) stream length N
Output: items with frequency counts exceeding (σ – ε) N
How much do we undercount?
  If stream length seen so far = N and bucket-size = 1/ε
  then frequency count error  # of buckets
  = N/bucket-size = N/(1/ε) = εN
Approximation guarantee
  No false negatives
  False positives have true frequency count at least (σ–ε)N
  Frequency count underestimated by at most εN

## Slide 26: Lossy Counting for Frequent Itemsets
Divide Stream into ‘Buckets’ as for frequent items, but fill as many buckets as possible in main memory one time
Bucket 1
Bucket 2
Bucket 3
  If we put 3 buckets of data into main memory, then decrease each frequency count by 3
Update summary data structure
  Itemset ( ) is deleted. That’s why we choose a large number of buckets–delete more
Pruning Itemsets – Apriori Rule
  If we find itemset ( ) is not frequent, we needn’t consider its superset
2
2
1
2
1
1
1
summary data
3 bucket data
in memory
4
4
10
2
2
0
+
3
3
9
summary data

## Slide 27: Other Issues and Recommended Readings
Other issues on pattern discovery in data streams
  Space-saving computation of frequent and top-k elements (Metwally, Agrawal, and El Abbadi, ICDT'05)
  Mining approximate frequent k-itemsets in data streams
  Mining sequential patterns in data streams
Recommended Readings
  G. Manku and R. Motwani, “Approximate Frequency Counts over Data Streams”, VLDB’02
  A. Metwally, D. Agrawal, and A. El Abbadi, “Efficient Computation of Frequent and Top-k Elements in Data Streams”, ICDT'05

## Slide 29: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 30: Classification for Dynamic Data Streams
Decision tree induction for stream data classification
  VFDT (Very Fast Decision Tree)/CVFDT (Domingos, Hulten, Spencer, KDD00/KDD01)
Is decision-tree good for modeling fast changing data, e.g., stock market analysis?
Other stream classification methods
  Instead of decision-trees, consider other models
    Naïve Bayesian
    Ensemble (Wang, Fan, Yu, Han. KDD’03)
    K-nearest neighbors (Aggarwal, Han, Wang, Yu. KDD’04)
    Classifying skewed stream data (Gao, Fan, and Han, SDM'07)
Evolution modeling: Tilted time framework, incremental updating, dynamic maintenance, and model construction
  Comparing of models to find changes

## Slide 31: Very Fast Decision Tree for Data Streams
Very Fast Decision Trees(VFDT) (Domingos, et al., KDD’00)
Hoeffding's inequality: A result in probability theory that gives an upper bound on the probability for the sum of random variables to deviate from its expected value
Based on Hoeffding Bound principle, classifying different samples leads to the same model with high probability—can use a small set of samples
Hoeffding Bound (Additive Chernoff Bound)
  Given: r: random variable, R: range of r, N: # independent observations
  True mean of r is at least ravg – ε,
      with probability 1 – δ
      (where δ is user-specified)
yes
no
Packets > 10
Protocol = http
Protocol = ftp
yes
yes
no
Packets > 10
Bytes > 60K
Protocol = http
Data Stream
Data Stream
Ack. From Gehrke’s SIGMOD tutorial slides

## Slide 32: Hoeffding Tree: How to Handle Concept Drifts?
Hoeffding Tree: strengths and weakness
  Scales better than traditional methods
    Sublinear with sampling
    Very small memory utilization
  Incremental
    Make class predictions in parallel
    New examples are added as they come
  Weakness
    Could spend a lot of time with ties
    Memory used with tree expansion
    Number of candidate attributes
Concept Drift
  Time-changing data streams
  Incorporate new and eliminate old
CVFDT (Concept-adapting VFDT)
  Increments count with new example
  Decrement old example
    Sliding window
    Nodes assigned monotonically increasing IDs
  Grows alternate subtrees
    When alternate more accurate: Replace the old one
  O(w) better runtime than VFDT-window

## Slide 33: Ensemble of Classifiers
Ensemble is a better way to handle concept drift than single trees
  H. Wang, W. Fan, P. S. Yu, and J. Han, “Mining Concept-Drifting Data Streams using Ensemble Classifiers”, KDD'03
Method (derived from the ensemble idea in classification)
    Train K classifiers from K chunks
    For each subsequent chunk
      train a new classifier
      test other classifiers against the chunk
      assign weight to each classifier
      select top K classifiers

## Slide 34: Issues in Stream Classification
Descriptive model vs. generative model
  Generative models assume data follows some distribution while descriptive models make no assumptions
  Distribution of stream data is unknown and may evolve, so descriptive model is better
Label prediction vs. probability estimation
  Classify test examples into one class or estimate P(y|x) for each y
  Probability estimation is better:
    Stream applications may be stochastic (an example could be assigned to several classes with different probabilities)
    Probability estimates provide confidence information and could be used in post processing

## Slide 35: Classifying Data Streams with Skewed Distribution
Problems of typical classification methods on skewed data:
  Tend to ignore positive examples due to the small number
  The cost of misclassifying positive examples is usually huge, e.g., misclassifying credit card fraud as normal
Classify data stream with skewed distribution (i.e., rare events)
  Employ both biased sampling and ensemble techniques
  Reduce classification errors on the minority class

## Slide 36: Concept Drifts
Changes in P(x, y) x-feature vector y-class label P(x,y) = P(y|x)P(x)
Four possibilities:
  No change: P(y|x), P(x) remain unchanged
  Feature change: only P(x) changes
  Conditional change: only P(y|x) changes
  Dual change: both P(y|x) and P(x) changes
Expected error:
No matter how concept changes, the expected error could increase, decrease, or remain unchanged
Training on the most recent data could help reduce expected error

## Slide 37: Stream Ensemble Approach
………
?
S1
S2
Sm
Sm+1
Classification Model
Sm as training data? Two few positive examples!
………
?
C1
C2
Ck
………
Biased Sampling
Ensemble
S1
S2
Sm
Ideas of Stream Ensemble
  Biased sampling: Save only the positive examples in the streams
  Ensemble: Partition negative examples of Sm into k portions to build k classifiers

## Slide 38: Experiments: Mean Squared Error on Synthetic & Real Data
Test on concept-drift streams (synthetic data)
Test on real data
Stream Ensemble always has lower error rate

## Slide 39: Experiments: Model Accuracy and Training Efficiency
Model accuracy
Training time

## Slide 41: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 42: Stream Clustering: A K-Median Approach
O'Callaghan et al. Streaming-Data Algorithms for High-Quality Clustering (ICDE'02)
Base on the k-median method
  Data stream points are from metric space
  Find k clusters in the stream such that the sum of distances from data points to their closest centers is minimized
A constant factor approximation algorithm
  In small space, a simple two-step algorithm
  For each set of M records, Si, find O(k) centers in S1, …, Sl
    Local clustering: Assign each point in Si to its closest center
  Let S’ be centers for S1, …, Sl with each center weighted by the number of points assigned to it
    Cluster S’ to find k centers

## Slide 43: Hierarchical Clustering Tree
Hierarchical Clustering Tree Method:
  Maintain at most m level-i medians
  On seeing m of them, generate O(k) level-(i+1) medians of weight equal to the sum of the weights of the intermediate medians assigned to them
data points
level-i medians
level-(i+1) medians
Concerns:
  Quality will suffer for evolving data streams (maintaining only m level-i medians)
  Limited functionality in discovering and exploring clusters over different portions of the stream over time

## Slide 44: CluStream: A Framework for Clustering Evolving Data Streams
C. Aggarwal, J. Han, J. Wang, P. S. Yu, A Framework for Clustering Data Streams, VLDB'03
Design goal of CluStream
  High quality for clustering evolving data streams with rich functionality
  Stream mining: One-pass over the stream data, limited space usage, high efficiency
The CluStream Methodology
  Tilted time frame work: otherwise, will lose dynamic changes
  Micro-clustering: better quality than k-means/k-median
    Incremental, online processing, and maintenance
  Two stages: micro-clustering and macro-clustering
    With limited overhead to achieve high efficiency, scalability, quality of results, and power of evolution/change detection

## Slide 45: Pyramidal Tilted Time Frame Adopted by CluStream
Pyramidal tilted time frame:
  Example: Suppose there are six frames (d = 5) and each takes a maximal of three snapshots
  Given a snapshot number N
    If N mod 2d = 0, insert into the frame number d
    If there are more than three snapshots, eliminate the oldest one
Snapshots of a set of micro-clusters are stored following the pyramidal pattern
  They are stored at differing levels of granularity depending on the recency
Snapshots are classified into different orders varying from 1 to log(T)
  The i-th order snapshots occur at intervals of αi where α ≥ 1
    Only the last (α + 1) snapshots are stored
Frame no. | Snapshots (by clock time)
0 | 69 67 65
1 | 70 66 62
2 | 68 60 52
3 | 56 40 24
4 | 48 16
5 | 64 32

## Slide 46: The CluStream Framework: A Micro-Clustering Approach Using the BIRCH CF-Tree Structure
CF1
child1
CF3
child3
CF2
child2
CF6
child6
CF1
child1
CF3
child3
CF2
child2
CF5
child5
CF1
CF2
CF6
prev
next
CF1
CF2
CF4
prev
next
B = 7
L = 6
Root
Non-leaf node
Leaf node
Leaf node
A CF tree: A height-balanced tree that stores the clustering features (CFs)
The non-leaf nodes store sums of the CFs of their children
Micro-clusters stored in CF-Tree
  Statistical information about data locality
  Temporal extension of the cluster-feature vector
  Multi-dimensional points with time stamps
  Each point contains d dimensions, i.e.,
  A micro-cluster for n points is defined as a (2d + 3) tuple

## Slide 47: CluStream: Clustering Evolving On-Line Data Streams
Divide the clustering process into online and offline components
  Online component (micro-cluster maintenance)
    Periodically store summary statistics about the stream data
      Initially, create q micro-clusters
        q is usually significantly larger than the number of natural clusters
      Online incremental update of micro-clusters
        If new point is within max-boundary, insert into the micro-cluster
        Otherwise, create a new cluster
        May delete obsolete micro-clusters or merge two closest ones
Offline component (query-based macro-clustering)
  Answers various user questions based on the stored summary statistics
  Based on a user-specified time-horizon h and the number of macro-clusters k, compute macro-clusters using the k-means algorithm

## Slide 49: Mining Data Streams
What is stream data? stream data management systems? and stream data mining?
Stream data cube and multidimensional OLAP analysis
Stream frequent pattern analysis
Stream classification
Stream cluster analysis
Summary

## Slide 50: Summary: Stream Data Mining
Stream data mining and stream OLAP analysis:
  Real life problem: Effectiveness, efficiency and scalability
Stream OLAP
  A multi-dimensional stream analysis framework
  Time is a special dimension: Tilted time frame
  What to compute and what to save?—Critical layers
  Partial materialization and precomputation
Stream data mining
  Mining frequent patterns
  Stream classification
  Stream cluster analysis

## Slide 51: References on Stream Data Mining (I)
C. Aggarwal, J. Han, J. Wang, P. S. Yu, “A Framework for Clustering Data Streams”, VLDB'03
C. Aggarwal, J. Han, J. Wang, P. S. Yu, “On-Demand Classification of Evolving Data Streams”, KDD'04
C. Aggarwal, J. Han, J. Wang, and P. S. Yu, “A Framework for Projected Clustering of High Dimensional Data Streams”, VLDB'04
S. Babu and J. Widom, “Continuous Queries over Data Streams”, SIGMOD Record, Sept. 2001
B. Babcock, S. Babu, M. Datar, R. Motwani and J. Widom, “Models and Issues in Data Stream Systems”, PODS'02.
Y. Chen, G. Dong, J. Han, B. W. Wah, and J. Wang, “Multi-Dimensional Regression Analysis of Time-Series Data Streams”, VLDB'02
P. Domingos and G. Hulten, “Mining high-speed data streams”, KDD'00
A. Dobra, M. N. Garofalakis, J. Gehrke, and R. Rastogi, “Processing Complex Aggregate Queries over Data Streams”, SIGMOD’02
J. Gehrke, F. Korn, and D. Srivastava, “On computing correlated aggregates over continuous data streams”, SIGMOD'01
J. Gao, W. Fan, and J. Han, “A General Framework for Mining Concept-Drifting Data Streams with Skewed Distributions”, SDM'07

## Slide 52: References on Stream Data Mining (II)
S. Guha, N. Mishra, R. Motwani, and L. O'Callaghan, “Clustering Data Streams”, FOCS'00
G. Hulten, L. Spencer and P. Domingos, “Mining time-changing data streams”, KDD’01
S. Madden, M. Shah, J. Hellerstein, V. Raman, “Continuously Adaptive Continuous Queries over Streams”, SIGMOD’02
G. Manku, R. Motwani, “Approximate Frequency Counts over Data Streams”, VLDB’02
A. Metwally, D. Agrawal, and A. El Abbadi. “Efficient Computation of Frequent and Top-k Elements in Data Streams”. ICDT'05
S. Muthukrishnan, “Data streams: algorithms and applications”, Proc 2003 ACM-SIAM Symp. Discrete Algorithms, 2003
R. Motwani and P. Raghavan, Randomized Algorithms, Cambridge Univ. Press, 1995
S. Viglas and J. Naughton, “Rate-Based Query Optimization for Streaming Information Sources”, SIGMOD’02
Y. Zhu and D. Shasha. “StatStream: Statistical Monitoring of Thousands of Data Streams in Real Time”, VLDB’02
H. Wang, W. Fan, P. S. Yu, and J. Han, “Mining Concept-Drifting Data Streams using Ensemble Classifiers”, KDD'03